## Slide 1: The IEEE 802.1 Standards
Tony Jeffree, 802.1 WG Chair
tony@jeffree.co.uk

## Slide 2: MENU
What is 802.1?
The Bridging standards
  “Traditional” Bridging
  Audio Video Bridging (AVB)
  Data Center Bridging (DCB)
The Security standards
Where to find out more
Backup slides

## Slide 3: What is 802.1?
Keeper of the LAN architecture – IEEE Std 802
  Describes the 802 family of standards
  Describes the LAN architecture
  Defines some useful things, such as the LAN address format, the SNAP protocol, the “Playpen Ethertypes”, and the OID registration arcs
The “Higher Layer Interface” working group in 802
  Defines the Bridging and security “glue” that interconnects the LANs defined by the 802 MAC groups

## Slide 4: The 802 LAN Architecture
Phy
Phy
Phy
Phy
MAC
MAC
LLC
LLC
MAC
MAC
RELAY
LAN
LAN
Physical
Link
Network
Transport
Session
Presentation
Application
OSI reference model
(Higher
Layers)
(Higher
Layers)
MAC Bridge
End station
End station
MAC sublayer
Medium
Physical layer
MAC service
user
MAC service provider
LLC sublayer
7
6
5
4
3
2
1

## Slide 5: 802.1Bridging standards: The core Bridging standards
Two base standards: 802.1D:2004 (MAC Bridging) and 802.1Q:2005 (VLAN Bridging), but 802.1D will be subsumed into 802.1Q in a future revision
Support for LAN reconfigurations in 50ms or less (“Rapid Spanning Tree”)
  Cures the historical problem of slow reconfiguration times
  Makes Bridged Ethernet competitive as a means of offering metro services
Support for up to 4094 VLANs over a single Spanning Tree (SST) or over multiple (up to 64) Spanning Tree instances (MST)
  Provides options for load balancing
  Allows choice of how VLANs map to Spanning Trees

## Slide 6: 802.1Bridging standards: Provider Bridging
802.1ad:2005 Provider Bridging - supports metro-area “provider” bridged LANs that can (trivially) multiplex 4094 X 4094 distinct services
802.1ah:2008 Provider Backbone Bridging
  Adds a 24-bit I-SID giving ~16 million “service instance identifiers”
  Adds a tunnelling protocol (external MAC addresses are local to the backbone)
802.1aw:2009 Provider Backbone Bridge Traffic Engineering – supports the construction of “traffic engineered” backbone topologies, protection switching, etc. to serve the needs of large service providers.
802.1aj:2010 Two-port MAC Relay
  Simple 2-Port Bridge – no Spanning Tree support
  Acts as a “demarc” device between service provider and service user
  Can be used to translate between “true” Ethernet and emulated Ethernet services

## Slide 7: Provider Backbone Bridged LAN
Provider Backbone Bridged Network
Provider Bridged Network
Provider Bridged Network
Provider Bridged Network
802.1aj
802.1ad
802.1ah,
802.1aw

## Slide 8: 802.1Bridging standards: Management
802.1ag:2007 Connectivity Fault Management and 802.1Qaw:2009 Management of Data Driven and Data Dependent Connectivity Faults
  Fault-finding tools (continuity checks, loopback functions etc.) aimed at managing both service provider and service user networks
802.1ap:2008 MIB definitions for VLAN Bridges – defines the set of MIBs required in order to support SNMP-style management of all of the Bridging technologies covered by 802.1Q and 802.1D
  Configuration and statistics gathering tools

## Slide 9: Ongoing developments
P802.1aq Shortest Path Bridging
  Intent is to provide optimal use of the available bandwidth in the network
  Has caused a move away from distance-vector routing techniques to some variant of link state

## Slide 10: Why Shortest Path Bridging?
Rapid Spanning Tree confines traffic to a single Spanning Tree
  Unused LANs, therefore wasted bandwidth
Multiple Spanning Trees splits traffic across Spanning Trees by VLAN
  Better utilisation of bandwidth but still can be sub-optimal paths
Shortest Path Bridging allows connectivity trees to be created per source Bridge
  A tree rooted at a Bridge defines the shortest path from that Bridge to any other Bridge

## Slide 11: AVB: Bridging optimized for A-V traffic
Audio-visual applications in home and studio environments generate a particular set of QoS requirements
  The need to synchronize audio/video in several adjacent rooms/areas
  The need to prioritize AV traffic to ensure that it stays within latency/jitter bounds
  The need to minimize packet loss
Potentially an enormous market
  Home AV applications
  Studio/concert hall applications
  Large venues e.g., theme parks
Three standards published, one currently under development:
  802.1AS:2011 – Time synchronization
  802.1Qat:2010 – Stream reservation protocol
  802.1Qav:2009 – Forwarding and queuing for time sensitive streams
  P802.1BA – AVB Systems

## Slide 12: P802.1AS – Time Synchronization
A common notion of time is needed in order for distributed AV applications to synchronize
  Lip synch between audio and video streams
  Synch between different instruments in a band
  Synch between speakers in adjacent rooms playing the same music
  …etc.
AS protocol accurately measures the delay between adjacent network nodes, and distributes a common “master” time from an accurate clock
Resilient in the face of network reconfiguration
Based on IEEE Std 1588 with extensions to meet the particular needs of LANs

## Slide 13: P802.1Qat – Stream Reservation Protocol (SRP)
Provides a means of reserving bandwidth for streams
Ensures that the path from the stream originator (Talker) to the stream destinations (Listeners) is not oversubscribed
Ensures that a Talker does not start to use network resources for a stream until those resources have been allocated to the stream
Deals with re-assignment of resources on network reconfiguration

## Slide 14: P802.1Qav – Forwarding and Queuing for Time Sensitive Streams
Defines a “Credit-based shaper” de-queuing algorithm for use in Bridges
  Stream transmission possible only if credit is not exhausted
  Credit is accumulated in proportion to the reserved bandwidth on the Bridge port
  Has the effect of limiting the bandwidth that can be used for streaming to the amount reserved by SRP
  Ensures that stream traffic takes priority over all other traffic
  Ensures that the stream latency is bounded and can be calculated for a given configuration

## Slide 15: P802.1BA – AVB Systems
This defines a number of “profiles” for different components in the network
  Bridges
  “Talker” stations
  “Listener” stations
Each profile selects options from the base standards (802.1Q, 802.1Qat, 802.1Qav, 802.1AS, 802.3, 802.11…etc) that are appropriate for the component
The standard may also define additional functions that don’t have a convenient home elsewhere
  E.g., detection of unacceptable configurations

## Slide 16: DCB: Bridging optimized for the data center and virtualized systems
Data centre (“server farms”) and “backplane” use of Ethernet brings a new set of requirements for Bridging:
  Very stringent requirements on latency and jitter
  Active handling of congestion to avoid the impact of frame discard and retransmission
  Result: drive to invent new Congestion Management mechanisms in LANs
Virtualization in end stations and servers bring further challenges
  The need for simpler bridging and bridge port extension strategies that allow lightweight bridge implementations in virtualized systems and V-NICs
  The need to provide discovery and configuration mechanisms to support the connectivity required among virtual stations

## Slide 17: DCB standard developments – 1:
P802.1Qau, Congestion Notification:
  Defines a means of signalling congestion back to the source of congestion
  Result is minimal discard rate
P802.1Qaz, Enhanced Transmission Selection:
  Defines a means of bandwidth sharing among traffic classes

## Slide 18: DCB standard developments – 2:
P802.1Qbb, Priority-based flow control:
  Extends the existing 802.3 Pause to operate on a per-priority basis. Also involves a minor change to the 802.3 MAC control frame under P802.3bd.
P802.1Qbg, Edge Virtual Bridging:
  Extends the Bridging standards to support virtual machine developments within desktop and server systems
P802.1Qbh, Bridge Port Extension:
  Allows a single Bridge Port to be extended within an attached station in order to provide individual communication channels for multiple virtual stations.

## Slide 19: The 802.1 Security standards: 1
802.1X:2010 Port based Network Access Control:
  Defines a “Controlled Port” accessible only after EAP-based authentication, and an “Uncontrolled Port” accessible at any time
  2009 revision adds “key agreement” protocol
802.1AE:2006 MAC Security:
  Defines a means of securing data on an individual LAN segment
  Integrated with the key agreement and controlled/uncontrolled Port functions in 802.1X
802.1AR:2009 Secure Device Identity:
  Defines unique per-device identifiers
  Allows standard mechanisms to authenticate a device’s identity
  Facilitates secure device provisioning

## Slide 20: Security architecture

## Slide 21: More information is available on IEEE 802.1 standards and activities here…
http://www.ieee802.org/1/
Free PDF copies of IEEE 802 standards available from…
http://standards.ieee.org/getieee802/index.html
…but only 6 months after publication

## Slide 22: Backup slides

## Slide 23: Summary of 802.1 Standards and Projects (1) - Bridging
Base Bridging standards (published):
  IEEE Std 802.1D:2004, MAC Bridges
  IEEE Std 802.1Q:2005, Virtual Bridged Local Area Networks
Amendments to IEEE Std 802.1Q:2005 (published):
  IEEE Std 802.1ad:2005 – Provider Bridging
  IEEE Std 802.1ag:2007, Connectivity Fault Management
  IEEE Std 802.1ak:2007, Multiple Registration Protocol
  IEEE Std 802.1Q:2005 Cor 1:2008 (bug fix for 802.1ak)
  IEEE Std 802.1ah:2008, Backbone Provider Bridges
  IEEE Std 802.1ap:2008, MIB definitions for VLAN Bridges
  IEEE Std 802.1aj:2010, Two-port MAC Relay
  IEEE Std 802.1Qay:2009, Provider Backbone Bridge Traffic Engineering
  IEEE Std 802.1Qav:2009, Forwarding & Queuing for Time Sensitive Streams
  IEEE Std 802.1Qau:2010, Congestion Notification
  IEEE Std 802.1Qat:2010, Stream Reservation Protocol

## Slide 24: Summary of 802.1 Standards and Projects (2) - Bridging
Amendments to IEEE Std 802.1Q:2005 (active projects, with probable completion date):
  P802.1aq, Shortest Path Bridging (Working Group ballot; Completion Dec 2011)
  P802.1Qaz, Enhanced Transmission Selection. (Sponsor ballot; completion 2011)
  P802.1Qbb, Per-priority flow control. (Task Group ballot ; completion 2011)
  P802.1Qbc, Remote Customer Service Interface. (Sponsor ballot ; completion 2011)
  P802.1Qbe, Multiple I-SID Registration Protocol. (Working Group ballot ; completion 2011)
  P802.1Qbf, PBB-TE infrastructure protection. (Working Group ballot ; completion 2011)

## Slide 25: Summary of 802.1 Standards and Projects (3) - Security
Published standards:
  IEEE Std 802.1X:2010, Port-based Network Access Control
  IEEE Std 802.1AE:2006, MAC Security
  IEEE Std 802.1AR:2009, Secure Device Identity

## Slide 26: Summary of 802.1 Standards and Projects (4) – The rest…
Published standards:
  IEEE Std 802:2001, Overview and Architecture
  IEEE Std 802a:2003, Ethertypes for Prototype and Vendor-Specific Protocol Development
  IEEE Std 802b:2004 Registration of Object Identifiers
  IEEE Std 802.1AS:2011, Time Synchronization
Active projects:
  P802, Overview and Architecture (Revision project. Expected completion December 2011)
  P802.1AC, MAC Service Definition (Expected completion December 2011)

## Slide 27: “C” and “S” tags in 802.1Q
EtherType
DA/SA
EtherType
DA/SA
S-Tag
VID
Priority
User Data
Customer (C-) Tag:
C-Tag
C-Tagged Frame:
16 bits
12 bits
3 bits
VID
Priority
Service (S-) Tag:
16 bits
12 bits
3 bits
User Data
C-Tag
S/C-Tagged Frame:

## Slide 28: Simple provider network example
C2
C2
C1
C1
Customer Bridge
Provider Bridge
Provider Network
C2
Service VLANs
Service Tag added & removed here
Customer VLANs
802.1ad
802.1D or
802.1Q

## Slide 29: Service Instance tags (I-Tags) in 802.1ah
EtherType
Priority
Format
I-SID
I-Tag:
DA/SA
I-Tagged Frame:
16 bits
24 bits
4 bits
DA/SA
96 bits
From
encapsulated
frame
Addresses are local to
the Backbone Network
4 bits
I-Tag
User Data

## Slide 30: A Spanning Tree isn’t necessarily a Shortest Path
Bridge 1
Bridge 2
Bridge 6
Bridge 3
Bridge 4
Bridge 5
Active LAN segment
Inactive LAN segment

## Slide 31: Shortest Path Trees
Bridge 1
Bridge 2
Bridge 6
Bridge 3
Bridge 4
Bridge 5
Active LAN segment for tree rooted at Bridge 3
Inactive LAN segment
Active LAN segment for tree rooted at Bridge 6
P802.1aj Two-port MAC Relay
  Simple 2-Port Bridge – no Spanning Tree support
  Acts as a “demarc” device between service provider and service user
  Can be used to translate between “true” Ethernet and emulated Ethernet services